## Slide 1: Maps
A representation of the whole or a part of an area.
Notes: Webster’s New Collegiate Dictionary (1979)
Consider def. No. 2: something that represents with a clarity suggestive of a map
But maps themselves are not always clear!!
Planimetric vs. Topographic
Many TYPES/Variations - focus on topographic
GOAL:
Learn to read the maps that are most useful for wilderness travel.
TOPOGRAPHIC

## Slide 2: Planimetric No contour information
Notes: Travel to trailhead
380,000 miles in Forest Road System (2000)
47,000 miles of Interstate
1.4M miles unpaved in US
2.6M miles paved in US
https://www.cia.gov/library/publications/the-world-factbook/fields/2085.html

## Slide 3: Topographic Maps
Coverage
Colors
Contour Lines
Symbols
Scale/Distance
Direction
Marginalia
https://pubs.usgs.gov/gip/TopographicMapSymbols/topomapsymbols.pdf
Notes: Convey TONS of useful info
Mostly symbolic - some text
GOALS:
Identify individual features
Learn to anticipate character of the terrain

## Slide 4: Topographic Maps
Define: 7.5 Min. Series
Latitude
7 ½ min.
7 ½ min.
Longitude
60 minutes per degree
4/16/2018
4
Notes: 7 ½ Minute maps: ~6 mi. W-E
~9 mi. N-S
Mt. Rainier East: 6.25 mi W-E
8.5 mi N-S

## Slide 5: Maps Features
Notes: Colors
Contour Lines
Symbols
Distance
Direction

## Slide 6: Topographic Maps
Colors
Contour Lines
Symbols
Scale/Distance
Direction
Marginalia
Tell what is on the surface
tree cover
open area
water
man-made
Notes: COLORS
Obvious, hence color is…
Most immediate indicator of terrain type and cultural features
Brown = contours
Red/black = major/minor roads and trails
Green = forested
Blue = water
White = open terrain; glaciers/snowfields

## Slide 7: Topographic Maps
Colors
Contour Lines
Symbols
Scale/Distance
Direction
Marginalia
Notes: Terrain SHAPE and ELEVATION
 Single contour = constant elevation
 Several adjacent Lines describe …
terrain shapes
steep / gentle slopes
saddle – look at adjacent line shapes
 “Straight up / straight down”
perpendicular to contours
 “Traverse”

## Slide 8: Contour Lines (Shape) Shape of Lines = Shape of Terrain
line
spacing
curved =
rounded
abrupt V =
gully, ridge
adjacent line
shapes
ridge
gentle steep cliff
Notes: “Shape…”
 Contour lines describe Shapes of Landforms
Different attributes …
curved: can be convex hill or concave basin
line spacing …
adjacent line shapes – note ridge especially

## Slide 9: Contour Lines (Shape) Shape of Lines = Shape of Terrain
line
spacing
curved =
rounded
abrupt V =
gully, ridge
adjacent line
shapes
ridge
saddle
x
gentle steep cliff
Notes: (notes are on previous slide)

## Slide 10
Contour Interval = 40 ft
4200
4400
4400
4200
Contour Lines (Elevation)
Notes: INDEX vs. INTERMEDIATE

## Slide 11: Contour Lines (Elevation)
Contour Interval = 40 ft
4200
4400
Notes: What is happening in the circled zones?

## Slide 12: Topographic Maps
Colors
Contour Lines
Symbols
Distance
Direction
Identify useful details
5807T
springs
footbridges
surveying data
roads, trails
trailhead
Notes: Symbols provide useful details
Tell you what you may find
Can help check where you think you are
<click1> < “springs …”>
<click2> < footbridge >
Footbridges – spring hiking & high creeks
<click3> < survey point >
May NOT be at high point
<click4> < road, trail >
<click5> < trailhead >
Some features are implied … trailhead
<click Next Slide> Exercises

## Slide 13: Topographic Maps
Colors
Contour Lines
Symbols
Scale/Distance
Direction
Marginalia
Terminology:
Map Size
Map Scale
4/16/2018
13
Notes: Distance and Direction = 2 Important Items from Maps
Scale = ratio between measurements on the map and in the real world
Distance measured using the SCALE

## Slide 14
Topographic Maps: Scale
1 = 24,000 = 2000
Notes: 1 of any unit of distance on map is 24,000 units on the ground
Keep a fraction in mind when considering scale:
1/24000
Larger scale  greater detail shown

## Slide 15
1
.5
0
1
“As the crow flies”
distance from
Correy Creek at Lake Trail,
to Fellows Mountain?
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
15
Notes: Straight Line Distance
1. Measure with ruler
2. Lay distance measured against map scale bar
Interpolate for the distance.
  Fractional scale segments
  helps estimating

## Slide 16
1
.5
0
1
“As the crow flies”
distance from
Correy Creek at Lake Trail,
to Fellows Mountain?
1.0
+ 3/10
+ 0.07
1.37
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
16
Notes: (previous slide has notes)

## Slide 17
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
17
Notes: String? Use compass lanyard, or …

## Slide 18
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
Map courtesy of Tim Kirk
Measurement Animation – K Welton
string
4/16/2018
18

## Slide 19
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
19

## Slide 20
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
20

## Slide 21
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
21

## Slide 22
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
22

## Slide 23
Trail distance from
Correy Creek at Lake Trail,
to Mountaineer Hut?
1
.5
0
1
1.12
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
23

## Slide 24: Topographic Maps
Colors
Contour Lines
Symbols
Scale/Distance
Direction
Marginalia
4/16/2018
24
Notes: Datums (Horiz and Vert.)
Dates
Scale
Declination
Contour Interval
Abbreviated Legend

## Slide 25: Topographic Maps: Marginalia (LHS)
Notes: NAD27 CONUS = 1927 North American Datum, Continental United States.
Declination (outdated)
Reference Line tick marks

## Slide 26: Topographic Maps: Reference Lines
UTM Generally not North-South
2.5 min
2.5 min
Notes: Okay to use UTM as N-S lines if less than 1 from TN.

## Slide 27: Topographic Maps: Marginalia (RHS)

## Slide 28: Questions?

## Slide 29: Extra Slides

## Slide 30: Topographic Maps
Familiarization:
Trace trip
Study terrain
trailhead
Alta Mtn.
Rachel Lk.
Alta Pass
Park
Lakes
Box Canyon
4/16/2018
30
Notes: Using Topo’s – Trip Planning
-- Familiarize self:
-- start point and goal of trip
-- general lay of land:
---- ridges  heights,
---- water  bottom

## Slide 31: Topographic Maps
Familiarization:
Trace trip
Study terrain
trailhead
Alta Mtn.
Rachel Lk.
-- streams are low
-- ridges are high
4/16/2018
31
Notes: Using Topo’s – Trip Planning
-- Familiarize self:
-- start point and goal of trip
-- general lay of land:
---- ridges  heights,
---- water  bottom

## Slide 32: Topographic Maps
trailhead
Alta Mtn.
Box Canyon
4/16/2018
32
Notes: Using Topo’s – Trip Planning
-- Familiarize self:
-- start point and goal of trip
-- general lay of land:
---- ridges  heights,
---- water  bottom

## Slide 33: Topographic Maps
7 ½ min.
15 min.
Map “SIZE”
4/16/2018
33
Notes: First example was 7 ½ minute
Another common SIZE covers 15 minutes
RED LINE: Note the relationship

## Slide 34: Topographic Maps
1 : 24,000
1 : 69,500
Map  World
1” = 24,000”
= 3/8 mi.
1” = 69,500”
= 1.1 mi.
Map “SCALE”
4/16/2018
34
Notes: <click > < “map scale” >
“Map Scale”-- map length to real distance
<click > < Map  World >
1” on map  24,000”;
<click > divide by 12  2000’;
a bit less than half-mile
<click x2 > < 1 : 69,500 >
Another common scale for wilderness maps

## Slide 35: Topographic Maps
1 : 24,000
1 : 69,500
1 : 69,500
15 min.
7 ½ min.
7 ½ min. Map “SIZE”
Map “SCALE”
4/16/2018
35
Notes: Just saw two scales
Another map at 1 : 69,500 …
Ask – what’s different with larger 1 : 69,500?
<click > < minutes … >
Answer: Map Size

## Slide 36: Topographic Maps
Colors
Contour Lines
Symbols
Distance
Direction
Terminology:
Map Size “7 ½ minute”
7.5 MINUTE SERIES
Map Scale 1 : 24,000
SCALE 1 : 24,000
4/16/2018
36
Notes: <click1, 2 > < “map scale” & legend >
“Map Scale”-- map length to real distance
1” on map  24,000”; divide by 12  2000’;
< half-mile
<click3, 4 > < “map size” & legend >
“Map Size”-- how much area maps covers
“minute”, latitude & longitude
DEMO -- show Green Trails map
– same SIZE 7.5 min; diff SCALE, 1:69,000

## Slide 37
1
.5
0
1
Lake Trail
Correy Creek
Intersection Trail & Creek
Fellows Mountain
Mountaineer Hut
Map courtesy of Tim Kirk
Measurement Animation – K Welton
4/16/2018
37
Notes: Get familiar with map
<click each> <
Lake Trail
Correy Creek
intersection
Fellows Mtn
Mountaineer Hut
<click Next Slide>